From pfslip04.phil.uni-sb.de!news.dfki.uni-sb.de!news.coli.uni-sb.de!news.dfn.de!scsing.switch.ch!swidir.switch.ch!newsfeed.ACO.net!Austria.EU.net!EU.net!news.sprintlink.net!demon!btnet!news.compulink.co.uk!cix.compulink.co.uk!usenet Fri Jun  2 04:21:26 1995
Newsgroups: comp.sys.ibm.pc.hardware.comm
From: segcom@cix.compulink.co.uk ("SEG Communications")
Subject: FAQ : HIGH SPEED SERIAL CARD & 16550 UARTS - DOCUMENT
Organization: SEG Communications ( Modem Suppliers). London, England. 0181 959 3377
Date: Thu, 1 Jun 1995 16:11:35 GMT



    Technical Note : FAST SERIAL PORTS & 16550 UARTS
            Author : Michael Spalter
             Email : segcom@cix.compulink.co.uk
            Origin : United Kingdom, EC
     Last Modified : 1st June 1995
            Status : (c) 1995 Michael Spalter

      * PLEASE UPLOAD THIS FILE TO BULLETIN BOARD AND OTHER HOSTS *
         The filename should be FAST550.DOC or FAST550.ZIP etc.
                                ^^^^^^^^^^^    ^^^^^^^^^^^
    NOTE:  This  document  may  be distributed freely providing that all
    credits remain intact and that it is not modified in any  way.  This
    document is provided for information only and no support or warranty
    is offered by the author or publisher.

    * PLEASE SEE THE FINAL SECTION FOR DETAILS OF UART/Board SUPPLIERS *


                              ---------------
                              C O N T E N T S
                              ---------------

            0) INTRODUCTION
            1) What is a UART ?
            2) Why the sudden craze for high speed cards ?
            3) Why aren't normal PC ports good enough ?
            a) Internal PC Card Modems
            4) How would I know if I need a faster port ?
            5) Okay, I want one ! What should I buy ?
            6) Is there just one type of 16550 UART ?
            7) Replacing a soldered 16450/8250 UART
            8) Windows and buffered UARTS
            9) Serial Port configuration
           10) Notebook PCs
           11) Enhanced 'Intelligent' serial ports
           12) Supplier information

    INTRODUCTION
    ------------

    Fast  serial  cards  have  become  very  popular  lately  due to the
    proliferation of high speed (V32bis/V34) modems. Whilst the computer
    press have been keen to cover modems in general, little coverage has
    been given to  serial  cards  (they're  just  not  sexy  enough  for
    mainstream  articles).  This  means that, whilst many people want or
    need fast serial cards, there is much  confusion  about  them.  This
    document attempts to answer the most common questions asked.



    1) What is a UART ?
       ----------------

    Throughout this document, we will refer to something called a 'UART'
    (pronounced 'you-art').  As this is a very important  component,  it
    is important to understand what it is.

    A  UART  is  an IC (chip!) which takes parallel data from the PC and
    outputs it to the serial port as a timed serial stream of data.   It
    is  the  main component of the serial port; all other components are
    there to support the UART.  Here is a simple functional diagram:

        PC's BUS Slot   __________           Serial port
        1 ------------> |        |
        1 ------------> |  UART  |
        0 ------------> |        |
        1 ------------> |        | ---------> 11010001
        0 ------------> |        |
        0 ------------> |        |
        0 ------------> |        |
        1 ------------> |________|

    The diagram shows conversion of data from a  parallel  to  a  serial
    stream. Of course, serial ports can receive data as well as transmit
    it, so the UART also converts serial data back into parallel data.


    2) Why the sudden craze for fast serial ports ?
       --------------------------------------------

    Now that high speed modems (V32bis/V34) have become very common,
    many PC serial ports are having problems running fast enough to keep
    up  with the modems which can be driven at speeds of up to 57600 bps
    (bits per second).  A standard '8250 UART'  based  serial  port  (or
    one using a multi i/o chip) cannot run at that speed due to the load
    placed on a typical working PC. The '16450' UART is slightly better.


    3) Why aren't normal PC ports good enough ?
       ----------------------------------------

    Standard serial ports were designed  to  drive  mice,  plotters  and
    modems.  At the time, modems ran at speeds of up to 4800 bps, and we
    thought that was fast - anyone who has been using  modems  for  more
    than  5  years  will  remember how lucky we thought we were !

    Problems with serial ports arise for one main reason:

    PC's  are  busy  things,  with lots of interrupts to service. If the
    port is running at high speed, the PC may miss interrupts  generated
    by incoming data because it is 'busy doing other things' - this then
    means  that  the UART has nowhere to put the incoming byte and so it
    gets overwritten by the next byte received. This usually causes  CRC
    errors.  The faster you drive the port, the more CRC errors you will
    get.   This  is  almost  always  a  problem  if  you  multitask with
    MS-Windows or Desqview,  as  the  rapid  task  switching  keeps  the
    processor  very  busy.  So,  for  instance,  if you need to run your
    serial port at 38400 bps or higher under MS-Windows then it is  very
    likely that you will need a buffered serial port.

    The 16550 UART is designed to run at high speed; a 16550  chip  will
    run  happily  at  57600  bps or faster which is fast enough for most
    modems.  Having said that, since this  article  was  first  written,
    28800  bps  modems have become available, some of which will support
    serial speeds up to 230000 bps !  To run your serial port at  230000
    you need a special intelligent serial card. See section 11.

    Having  said  that, to achieve that sort of speed, you would need to
    attain 8:1 data compression @ 288000  bps  which  is  most  unlikely
    with  normal  data  and  if you really had data which would compress
    that much,  then you'd be better off compressing the
    file  with  PKZIP/ARC/LHA  or  another  file   compression   program
    beforehand. Typically, a 28800bps modem  with  V42bis  will compress
    data  at up to 4:1, but typically little over 3:1. Four times 288Kbps
    is 115200bps and a 16550 UART in a fast PC can run this fast. If you
    are sending compressed files (ZIP,ARC,LZH etc) then  they  will  not
    gain from your modem's data compression at all.

    The main reason that a 16550 UART can cope with PC's interupt  rates
    is  that  it incorporates a 16 byte buffer; if the PC isn't ready to
    received the current byte then the UART can retain it in the  buffer
    until the PC is ready for it.  16 bytes provides a comfortatble time
    margin  to  ensure  that  none  of  the received data is lost.  Many
    communications  packages  will  empty  the  FIFO  buffer  at   every
    interrupt  possible, rather than only taking one byte per interrupt.
    The buffer on the UART is a 'FIFO' buffer.  This simply  means  that
    the  first  byte  in  will be the first byte out. The alternative to
    this would be a LIFO buffer, but that would be useless for a UART as
    all the data would become scrambled !


    Analogy
    -------

    Imagine  a  mail  man  in the US collecting mail in a street. Assume
    that each mail box can only hold ONE letter and  that  people  raise
    their  'flag'  on their mail box to indicate that they have a letter
    for collection - the flag is equivalent to a PC's  'interrupt'.  The
    mail man sees the flag and runs along to collect the letter.

    If  there  is  a  certain level of mail being collected, then it all
    works well - the  mailman  has  enough  time  to  collect  all  mail
    (equivalent to servicing all interrupts).

    However,  if  someone  puts a letter in their box and the mailman is
    too busy to collect it before that same person has another letter to
    mail, then there is a problem: As the mail box  can  only  hold  one
    letter, they would have to destroy the first letter.

    This  is  how  a normal serial port works. A buffered serial port is
    simply a bigger mailbox, which can hold up to 16 'letters' at  once,
    so  that  when the mailman comes, he can collect up to 16 letters at
    once.


    ( NOTE : The author of this document is in England, where  we  don't
    have  mailmen who collect post from our houses - we have postmen who
    deliver post and red pillar boxes into which we deposit our  post  -
    the  system  referred to above is the one used in the US, because it
    wouldn't work with the UK system. Any non-US people unfamiliar  with
    these  'flags'  should  refer  to  a 'Peanuts/Charlie Brown' cartoon
    where they seem to feature  regularly.)


    3a) Internal (PC Card) Modems
        -------------------------

    Some  people  have  been confused about differences between internal
    (PC Card) and external (desktop) modems.  An  internal  modem  plugs
    into  a  normal expansion slot inside a PC. Instead of plugging into
    the PC's serial port, it has its own serial port  on  board  and  so
    takes its data directly from the PC BUS.  BUT REMEMBER : An internal
    modem  still  has a UART which, just like with a normal port, can be
    an 8250, 16450 or 16550 (or circuitry which behaves like one).

    An interal card modem can either have  a  physical  40-pin  UART  or
    sometimes it is embedded within another controller so you may not be
    able  to  spot  it by looking at the board. When buying a V32bis (or
    faster) internal card modem you should insist that it has  either  a
    true  16550  or  16550  'functionality'. You can test this using the
    '16550.EXE' program or if you have MS-Windows, the MSD program  will
    tell  you  which  type  of UART the modem has. This can of course be
    used to check the UARTs of regular serial cards too.

    External modems do not need to have buffered UARTS within the actual
    modem - the buffered UART is only required within the PC (either  on
    a  serial card or a modem card) because the flow control system used
    across the PC BUS is inadequate for modems (the interrupt method)  -
    once  the  data  is  in 'serial form' then flow control becomes much
    more reliable. For PCMCIA modems, see the later section.


    4) How would I know if I needed a faster serial card ?
       ---------------------------------------------------

    If you are multitasking using MS-Windows or Desqview, then you  will
    almost  certainly need a fast buffered serial card. Typical symptoms
    will be CRC errors or block retries reported when downloading files.
    As you will probably be using error correction,  then  these  errors
    are unlikely to be caused by anything else.

    Another  symptom  of an inadequate serial port is that you're simply
    not getting the performance you'd expect from your modem. This could
    be caused by you not having your modem configured correctly,  so  in
    the  first instance, check with your suppliers or colleagues/friends
    for any special setup strings particular to your modem (perhaps  you
    have  forgotten  to enable RTS/CTS handshaking or data compression).

    If  you  have your modem set up correctly and your performance still
    isn't what it ought to be, then a faster  serial  card  may  be  the
    solution.  On  a  V32bis/V42bis modem, you should be able to achieve
    download speeds of up to 3000 cps on ASCII  text,  or  1500  cps  on
    compressed  (e.g.  ZIP)  files.   Remember that poor phone lines can
    also affect modem performance.

    Even if you are not using Desqview or MS-Windows, you may still  get
    the  symptoms details above, especially if you are driving the modem
    at 38400 bps or faster, in which case you would be wise to invest in
    a faster serial card. Having said that, there are some people  using
    high  speed  modems  whose  existing serial port may be adequate, in
    which case there is no point investing in a faster one !

    A  fast  serial  card  with  a 16550 UART can be checked for using a
    number of commonly available utilities. If you have  MS-WINDOWS  3.1
    installed,  then  from DOS, you can run the MSD program which you'll
    find in your C:\WINDOWS directory. Under the option labelled 'Serial
    Ports' you can view your existing ports and MSD will report the UART
    type fitted (8250, 16450 or 16550).


    5) Okay, I want one, what should I buy ?
       -------------------------------------

    The  important part about a fast serial card is its UART; this means
    that you may be able to simply swap the UART of your existing serial
    card, rather than having to fit a whole new card.  You can  only  do
    this  if your current serial card uses a 40 pin UART (8250, 16450 or
    equivalent). This needs to be  socketed  for  easy  removal,  unless
    you're  particularly  experienced  with  a  soldering iron and fancy
    desoldering the chip yourself (see section 7).

    Unfortunately,  most PC's nowadays seem to come with multi i/o cards
    with one multi-purpose chip which performs serial, parallel and disk
    operations; if you have a multi i/o card, it will normally be a PLCC
    package in the centre of the board ( a flat 'surface  mounted'  chip
    with pins on all four sides). This obviously cannot be replaced with
    a  40-pin  16550  chip.  Some PC's have the i/o circuitry built into
    the motherboard; it is unlikely that you can replace the UARTs.

    Thankfully, and more easily, you can simply buy  a  new  card  based
    around a 16550 UART. This can either replace or add to your existing
    serial  ports and your supplier will advise you on the best type.


    6) Is there just one type of 16550 UART ?
       --------------------------------------

    No! As with all  semiconductors, many manufacturers have  jumped  on
    the 16550  bandwaggon. This is good inasmuch that there is a choice,
    but bad in that some manufacturers have got it  wrong  -  some  have
    FIFO  buffers which don't work and some aren't  recognised correctly
    by applications (this can sometimes be worked around but ideally get
    one which you know will work).

    The 16550 chip 'by which others are  gauged'  is  made  by  National
    Semiconductor,  and the original part no.  was NS16550AFN.  However,
    due to the increasing popularity of the chip, NS decided  to  change
    the  name.   The  latest  version  is  now the PC16550DN. There were
    earlier version of the original 16550 which didn't  work  correctly,
    but it is highly unlikely that any of these are still around (it was
    the NS16550N - i.e. not the 'AN' or 'AFN').

    Other  manufacturers  have now brought out their own 100% compatible
    versions of the NS UART, so you may find that your supplier stocks a
    different version, some of which work well, others don't.   As  long
    as  your dealer guarantees 100% compatibility it should work as well
    as the NS original.  Many 'clones'  are  made  in  what's  known  as
    'CMOS'  versions.  They are functionally identical (CMOS chips users
    less power) so they should work fine too. A CMOS UART will  normally
    be called a '16C550' or similar.  Being the original, the NS type is
    the  most  expensive  16550 UART, so you will probably save money by
    buying a clone, but take note of the above guidelines.

    The  FIFO  buffer  on  a  16550 chip can be enabled and disabled. By
    default it will be DISABLED. Many comms programs will  automatically
    detect  and  enable the FIFO buffer, but if yours doesn't, there are
    several programs to enable them,  which  you  can  include  in  your
    AUTOEXEC.BAT  file  or another batch file. Ask your supplier. If you
    are running under MS-Windows then see section 8.

    There are several programs around to test 16550 chips, once they are
    installed  so you'll soon know if your new chip/card is okay. If you
    can't get hold of one, ask around on BBS's  or  ask  your  supplier.
    MSD.EXE  is  supplied  with Windows 3.1 and will detect/report 16550
    UARTS, but there are a couple of problems with MSD; see Section 8.


    7) Replacing a soldered 8250 or 16450 UART
       ---------------------------------------

    If your existing UART is a soldered 16450 or 8250 type  (40 pin DIP)
    and  you  are  competant  with  a  soldering  iron then we recommend
    snipping the pins of the existing UART and then  removing  the  legs
    one by one. Then fit a socket before you insert the 16550 UART.


    8) MS-WINDOWS and high speed UARTS
       -------------------------------

    Microsoft Windows is a prime cause  of  lost  interrupts.   This  is
    partly  due  to  the fact that MS-Windows is processor intensive but
    mostly because of the way that  MS-Windows  multi-tasks.  MS-Windows
    uses  a  system of co-operative multi-tasking whereby an application
    is given control of the processor until it decides to pass it on  to
    the  next  application.   As  such,  if  an application is 'hogging'
    processor time and bytes are arriving at the serial port for another
    application, they'll have nowhere to go. In  future  generations  of
    MS-Windows,  a  more  reliable  system of 'time slice' multi-tasking
    will be used where each application is  given  a  little  processing
    time   and   then  control  is  automatically  passed  to  the  next
    application; this is how Desqview and OS/2 work currently.

    A  properly  configured  16550 UART  should  solve  these  problems;
    MS-Windows  is  16550 aware, though you may need to make a couple of
    modification to your SYSTEM.INI file to enable the 16550,  otherwise
    it will run in '16450 compatible mode' and you'll get no benefit.

    Once you have installed your 16550 UART  or  16550  equipped  serial
    card,  the  Microsoft  MSD program can be used to check it. MSD is a
    DOS program which you'll find in your WINDOWS directory; it must  be
    run  from  the  DOS prompt, not from within Windows itself. Remember
    that if you installed your serial card to use  a  non-standard  IRQ,
    you set it up with the 'Ports' option within Windows Control Panel.

    If you look at your serial ports, it will show the type of UART each
    is fitted with. If you have selected non-standard IRQs or you have a
    COM4  but  no  COM3, MSD gets confused, so if it doesn't display the
    expected results, don't panic !

    Next, you'll need to edit your SYSTEM.INI file. You can do this from
    DOS using any suitable text editor or from  within  Windows  Program
    Manager,  select  'FILE'  then  'RUN'  and  enter  SYSTEM.INI as the
    filename.  Windows' text editor will load your SYSTEM.INI file.

    Find the section  within  SYSTEM.INI  labelled  '[386Enhanced]'  and
    check for a line which reads:

    COMxFIFO=1

    where  'x'  will be the COM port with your 16550 fitted; chances are
    that line won't exist, in which case you should add it. If there are
    other lines beggining with COMx... then it makes sense  to  add  the
    new  line  near them. For instance, if your 16550 UART was fitted to
    COM3, you would add the line:

    COM3FIFO=1

    When  using  the  standard  Windows  COMM driver, there are no other
    options other than '1' here as  it  is  a  boolean  setting  (either
    False=0 or True=1).

    When using Windows, there is  no  need  to  enable  the  16550  UART
    buffers  manually with any programs such as 16550.EXE. In fact, with
    Windows 3.1,if you enable the UART's FIFO buffers (using a 16550.EXE
    or whatever) before Windows, then it won't recognise the COM port.

    A company call CyberSoft, in Australia have produced  a  replacement
    comms  driver  for  MS-Windows  3.1  which claims to improve Windows
    comms performance and make best use of the 16550. The driver may  be
    used  for  free  in non-commercial enviroments. Contact Cybersoft on
    email at : 100033.1723@compuserve.com.  Also, Delrina,  the  company
    who  make  the  'Winfax'  software  have their own replacement comms
    driver called WFXDRV.DRV (or similar) which also claims to  improved
    Windows  comms  performance.  WFXDRV is available from many bulletin
    boards as well as Cix and Compuserve.


    DOS Applications Under Windows
    ------------------------------

    A  slight  bug  with  Windows 3.1 is that if you enable your 16550's
    FIFO  buffers  before  running  Windows,  then  the  port  will   be
    unavailable,  so make sure you don't enable the FIFOs before you run
    Windows !  Any DOS comms program should be able to take advantage of
    the 16550, but ideally the DOS software  will  have  specific  16550
    support to enable multiple bytes to be read on each interrupt.


    9) Serial Port Configuration
       -------------------------

    This  section is relevant to all standard serial cards, whether they
    are 16550 based or the normal 8250/16450 types. See section  11  for
    details of 'intelligent' high speed serial boards.

    There  are  only  two  IRQ's  officially allocated for serial ports,
    namely IRQs 3 and 4. In theory, this means that  you  can  therefore
    only  have  a  maximum  of two serial ports. You can have more (i.e.
    COM3  and  COM4)  by  sharing  the  interrupts  (although  different
    addresses),  but  this  causes problems for modems as you cannot use
    the ports simultaneously when sharing  interrupts  unless  they  are
    being controlled by the same application.

    Some serial cards allow you to select non-standard IRQ's,  typically
    any  of  2,3,4,5,7  or 9 (10-14 are sometime available on 16-bit ISA
    cards).  You can only use non-standard IRQs if your software  allows
    you  to  and also if that IRQ setting doesn't clash with another i/o
    card already installed. IRQs 5 and 7 are allocated for the  parallel
    ports,  but  often not used, so they may be available.  Higher IRQ's
    are only available on 16-bit cards as the IRQ hardware lines are  on
    the   second   part  of  the  BUS.  MS-Windows  allows  you  to  use
    non-standard IRQs by setting them from Windows 'Control Panel.'

    Typically, if you are adding a third serial port to your PC, and you
    can't  use  non-standard  IRQs,  set  your new card as COM3/IRQ4 and
    don't use your existing COM1 as it shares interrupts -  as  long  as
    there's   nothing   connected  to  a  port,  it  shouldn't  generate
    interrupts.  If you need to use your existing COM1, you can put your
    new card in as COM4/IRQ3, but then you can't use  your  COM2  as  it
    shares its interrupt with COM4.

    Always  experiment  though; an interrupt clash will at worst prevent
    your machine booting (temporarily!).  If  all  else  fails,  disable
    your  existing COM1 or COM2 (there should be some jumpers on the i/o
    card) and put your new card in as COM1 or 2.

    Windows Users : If you fit your third port as COM4, the MSD  program
    will  report  it as COM3 due to the way DOS stores the addresses for
    COM ports; don't worry, the port  still  works.   When  MSD  reports
    'COM3'  what  it  actually  means is 'your third serial port'. Other
    programs may report similarly.


    10) Notebook PCs
    ----------------

    Users  of  Notebook  PCs often want to upgrade their serial ports to
    buffers types.  The most common answer is that you  can't;  to  save
    space,  notebooks  use  multi-function chips, so the chip which does
    the serial i/o will have  many  other  function  too  and  so  isn't
    replaceable.

    Worse  still,  notebooks can't take normal PC expansion cards so you
    can add additional ports, unless your notebook has a docking station
    option which can take cards. Also, many Notebook PCs have  dedicated
    modems  which  fit  into  propritary slots; again the UARTs on these
    modems cannot be changed, though any sensible V32bis modem  designer
    would have included 16550 functionalty in his modem design.

    The  only solution to a notebook PC without buffered serial ports is
    to fit a PCMCIA modem if you have a PCMCIA slot. As  well  as  being
    very  neat  and  compact,  many  V32bis  PCMCIA modems include 16550
    functionality - to check the Microsoft  MSD  utility  or  any  other
    16550  checker should confirm the presence of it. If you wish to use
    a normal modem with a notebook PC,  then  some  companies  now  make
    PCMCIA  16550 based serial ports which give you a normal serial port
    for a regular modem.


    11) Enhanced Serial Ports
    -------------------------

    This document is dedicated to 16550-based serial cards,  but  it  is
    sensible  that  we  cover the alternatives. There is another type of
    serial card which has an on-board  processor  and  using  inteligent
    program to card communication, comms becomes entirely controlled and
    100%  reliable  in almost all circumstances, even when a traditional
    16550 won't work (particularly if you need 115200 or 230400 bps).

    Several serial port  cards  have  been  announced  which  solve  the
    problem of lost characters on receive by implementing automatic flow
    control  independent  of the software running on the PC. These cards
    have some sort of processor on the card which can determine when the
    buffers are filling up and ask the modem to stop  sending.   In  the
    case  of a 16550-based card, if the 16-byte buffer isn't big enough,
    it just overflows. This will only happen if you are really trying to
    run the card at very high  speeds  and  the  16-bytes  are  normally
    enough for speeds up to 115200 bps.

    Usually,  the 'intelligent' cards have extra buffer capacity so that
    flow control events can  be  reduced  in  number.  This  idea  is  a
    solution to the problem of lost data but it does not always increase
    the  throughput  significantly  because  the limitation is often how
    quickly the comms software can get the data.

    Newer port cards, like the Hayes ESP, can  transfer  data  from  the
    card  to  the  PC memory in better ways than that used by normal com
    port cards. This type of approach is like the techniques used in LAN
    cards or disk controllers. Unfortunately, the comms software has  to
    support the card directly if it is a DOS application, however, if it
    is  a  Windows  application,  a replacement comms driver will be all
    that is necessary; any software that uses the Windows comms API will
    then be able to take advantage of the higher throughput.

    So when would you need one of these cards in preference to a regular
    16550 based card ?  There are several circumstances:

    1. If you experience lost characters with a 16550.

    2. If you are running many processor-intensive Windows  applications
    at the same time.

    3.  If  your  modem or ISDN adaptor can pass data faster than 115200
    bits/s. (The Hayes ESP2 goes up to 921.6 kbit/s !).

    4. If you want to use MORE than two COM ports simultaneously.

    Intelligent  serial  port  cards  are  more  complicated than normal
    16550-based cards and  therefore  cost  considerably  more  but  the
    typical street price of all of them is well under 100 pounds.

    There are only a handful of companies making  enhanced  serial  port
    cards  for  PCs.   The  most  popular  one  by  far is the Hayes ESP
    (Enhanced Serial Port) card. By default, the ESP card runs in '16550
    compatible mode' but by installing Hayes'  special  Windows  driver,
    you can take advantage of the very high reliable speeds.



    12) Supplier information
       --------------------

    SEG Communications, based in London, England, stock a range of 16550
    UARTs,  16550  based  serial  cards  and  the Hayes ESP card at very
    competitive prices. We can ship worldwide.

    For full details and pricing information contact:

            SEG Communications
            137 Hale Lane
            Edgware
            Middlesex HA8 9QP
            England, U.K.
            Tel: (0181) 959 3377
            Fax: (0181) 959 2137

            Email: segcom@cix.compulink.co.uk

      From outside the UK, Fax : + 44 181 959 2137


      Popular Model : SC5500 Serial Card; Single port card.
                      COM 1,2,3,4 Selectable IRQ 3,4,5,7,9
                      Fitted with one 16550 UART.

    SEG  also  sell HAYES ESP cards as detailed in section 11 and a full
    range of desktop, pocket, PC Card and PCMCIA modems and adaptors.


            ------------------ End of Document ----------------


    (c) 1993/4 Michael Spalter, SEG Communications

    This  document may only be distributed un-modified.  Reproduction as
    part  of  any  commercial  transaction  or  distribution   via   any
    non-electronic  medium is prohibited in part of full without written
    permission  from  the  author.  This  file  may  not  be compiled or
    included within any other document  or  help  system  without  prior
    written permission from the author.

    If you have enjoyed  this  document  or  have  any  suggestions  for
    improvement, you can contact the author by Email.

                          ----- end of file -----